## Slide 1
Comparative Analysis of
Distance-Vector & Link-State Routing Protocols
Based on RIP and OSPF
Group 2:
FU Jintao GUO Xiaofan LIN Yingqi
LIU Yang YIN Chenghao ZHAO Chao
18 / 01 / 2024
IR.1101 - Réseaux/Networks
Final Project
PRESENTATION

## Slide 2
TABLE OF CONTENT
Introduction
Routing Protocol
  Distance-Vector Routing Protocol (RIP)
  Link-State Routing Protocol (OSPF)
  Comparative Analysis
Implementation
  Small-Scale Network (Suitable for RIP)
  Large Enterprise Network (Suitable for OSPF)
  Hybrid Network (Coexistence of RIP and OSPF)
Conclusion

## Slide 3
1.Introduction
Dynamic routing protocols are essential in modern networking, allowing routers to exchange information dynamically, enabling networks to adapt seamlessly to changes.
Protocol Categories
  Distance-Vector and Link-State protocols are distinguished by their wide adoption and unique operational mechanisms.
Focus on RIP and OSPF
  This presentation will concentrate on two protocols: the Routing Information Protocol (RIP) and Open Shortest Path First (OSPF).
Monitoring and Distribution
  Monitoring network changes and distributing this information across routers, making the choice of a suitable routing protocol a key decision in network design and management.

## Slide 4
Operate at 3rd of OSI model(Network Layer)
Purpose: sorting & distribution of IP packets
Attribute and Characteristics:
  Best Possible Routers
  Faster Convergence
  Security Options
  Avoiding Loops
Dynamic Route: selected using routing protocol
IGP(Interior Gateway Routing Protocols)
  Use for route selection within the autonomous system
  Each of routing protocol has their own metric & administrative distances
2.Routing Protocol
Figure Source: Khan, Murad; Javaid, Nadeem. (2019, February). “Routing in IP-based Networks.” Thesis. pp.10.[51].

## Slide 5
2.1Distance-Vector Routing
The DV Routers
  Not know about the complete network topology
  Only have info passed by the neighbour devices
  The characteristics of DVR protocol
    Bellman-Ford Algorithm
    Metrics: Distance and Vector (mainly based on Hop-Counts vector)
    Defines Routing Table (neighbor routers direct connection)
    Periodic Updates
    Simple and Efficient
    Pros and Cons of DVR
      Simple Algorithm
      Easy To Implement
      Occupies Less Memory & Processor
      Loops May Occur
      Regularly Updated
      Single Parameter
Figure Source: Khan, Murad; Javaid, Nadeem. (2019, February).
“Routing in IP-based Networks.” Thesis. pp.16.[51].

## Slide 6
2.1.1Routing Information Protocol
RIP：
Suitable for small IP networks.
Use hop-count as metric (up to 15 hops)
Convergence time required
Low memory and processor requirements
Routing loops may occur during network failures
Figure Source: Khan, Murad; Javaid, Nadeem. (2019, February).
“Routing in IP-based Networks.” Thesis. pp.3.[51].

## Slide 7
2.2Link-State Routing
  The characteristics of LSR protocol
    SPF (Shortest Path First Algorithm) [Dijkstra’s Algorithm]
    Precise Metrics(Bandwidth, Delay and other QoS parameter)
    Identical Database
    Provides Hierarchical Structure
    Triggered Update
    Efficient and Fast Convergence Without Any Loop
    Pros and Cons of LSR
      Respond Quickly
      Small Packet Size
      Complex Algorithm
      High Memory Consumption & Processor Requirements
      Difficult to Configure
      Poor Performance on Constantly Changing Links
Figure Source: Khan, Murad; Javaid, Nadeem. (2019, February).
“Routing in IP-based Networks.” Thesis. pp.14.[51].

## Slide 8
2.2.1Open Shortest Path First
OSPF:
Suitable for large networks or environments that require rapid convergence
Specifically designed for IP networks, so IP routing is calculated directly
Calculating costs mainly relies on bandwidth
Figure Source: Khan, Murad; Javaid, Nadeem. (2019, February).
“Routing in IP-based Networks.” Thesis. pp.33.[51].

## Slide 9
2.3Comparative Analysis

## Slide 10
3.Implementation
Use Cisco to build the following simulation scenario:
3.1 Small-Scale Network (Suitable for RIP)
3.2 Large Enterprise Network (Suitable for OSPF)
3.3 Hybrid Network (Coexistence of RIP and OSPF)
Notes: To gain a comprehensive understanding of dynamic routing protocols, particularly the distinctions between RIP and OSPF.

## Slide 11
3.1Small-Scale Network (RIP)
Build a Small-Scale Network

## Slide 12
Ping PC1 from PC0 failed,
Ping Router0 from PC0 succeeded.
Because RIP is not configured yet
→ nework0 and network1 cannot communicate.
3.1Small-Scale Network (RIP)

## Slide 13
Configure RIP on Router1 and Route0 save it.
3.1Small-Scale Network (RIP)

## Slide 14
Ping PC1 from PC0 failed the first time
Ping succeeded the second time.
Because it takes time for the RIP protocol to update the routing table.
3.1Small-Scale Network (RIP)

## Slide 15
Check Routing Table of R1
3.1Small-Scale Network (RIP)

## Slide 16
Check HOP form PC0 to PC1
3.1Small-Scale Network (RIP)

## Slide 17
3.2Large Enterprise Network (OSPF)
Build a simplified single-area OSPF network

## Slide 18
Configure OSPF protocol on routers
3.2Large Enterprise Network (OSPF)

## Slide 19
Stimulate the OSPF network
3.2Large Enterprise Network (OSPF)

## Slide 20
Build the multi-area OSPF network
3.2Large Enterprise Network (OSPF)

## Slide 21
Configure OSPF protocol on routers
3.2Large Enterprise Network (OSPF)

## Slide 22
Stimulate the netork
3.2Large Enterprise Network (OSPF)

## Slide 23
Advantage
  Scalability
  Efficient Routing
Disadvantages
  Complexity
  Resource Intensive
3.2Large Enterprise Network (OSPF)

## Slide 24
Redistribution
3.3Hybrid Network (RIP and OSPF)
Convert RIP and OSPF metrics to make them compatible

## Slide 25
Configure RIP for the router in Area2
Specify the network participating in RIP
3.3Hybrid Network (RIP and OSPF)

## Slide 26
Configure OSPF for the router in Area 0 and Area 1
OSPF area division
The OSPF process numbers of adjacent routers must be the same.
3.3Hybrid Network (RIP and OSPF)
R3
R1

## Slide 27
Configure OSPF redistribution into RIP
Border router
Router that performs route redistribution
3.3Hybrid Network (RIP and OSPF)

## Slide 28
Configure OSPF redistribution into RIP
Redistribute RIP routing information in the OSPF process
OSPF incorporates the subnet information learned by RIP into the OSPF routing table
Redistribute OSPF routing information in the RIP process
The imported OSPF route will be set with a metric value of 10 instead of using the default RIP hop count.
3.3Hybrid Network (RIP and OSPF)

## Slide 29
Verify network connectivity
3.3Hybrid Network (RIP and OSPF)

## Slide 30
Advantages
Interoperability: Supports legacy systems where RIP is already in place, allowing for a smoother transition to more advanced OSPF without immediate full-scale upgrades.
Flexibility: Enables phased network upgrades, transitioning individual segments to OSPF while maintaining overall network service.
Cost-Effectiveness: May defer costs associated with upgrading hardware that does not support OSPF.
Disadvantages
Complexity: Managing two protocols increases the complexity of the network, necessitating advanced knowledge and careful configuration to prevent issues like routing loops and asynchronous routing tables.
Inconsistency in Metrics: OSPF and RIP use different metrics for determining the best path, which can lead to suboptimal routing decisions when the protocols interact.
Administrative Overhead: Requires careful tuning of redistribution between the protocols to maintain a consistent and loop-free environment.
3.3Hybrid Network (RIP and OSPF)

## Slide 31
How Choosing Between RIP and OSPF:
Depends on network size, complexity, and requirements for efficiency and scalability.
Each protocol has its specific use case and operational objectives.
4.Conclusion
 | RIP | OSPF
Scale | Small | Large
Complexity | Low | High
Overhead | High in bandwidth Low in computation | Low in bandwidth High in computation
User friendly | High | Low
Notes: 怎么选择？