## Slide 1: Optical Fibre networks 1/4 Optical Fibre : characteristics
Paul JOLIVET
30/09/2024

## Slide 2: Optical Fibre Networks : Course general objective
Get a panorama of Optical Fibre and networks
  Optical Fibre characteristics and advantages
  Technologies around Optical Fibre
  Other components of optical fibre networks
Understand How to design high rates optical fibre networks
  Existing architecture of Optical Fibre networks (FTTH, FTTA, FTTO…)
  Designing a network
  Deployment constraints
Understand High rate networks trends to future

## Slide 3: Optical Fibre Networks : Course organisation
Programme
  Course : 4 sessions (3h each) on Sept 30, Oct 7 and Dec 2 & 16
  Project : 2 sessions with support on Oct 14 & Nov 18
  Project Defence : Jan 13
  Exam (no information on the schedule)
Two type of session with me
  Course
  Application on a project
    A teamwork with contributions from all members
    Practical use of the knowledge share in the courses
    Search work on the internet
    Support from teacher
    Defence in English with slideshow and share of the speech between team members

## Slide 4: Optical Fibre Networks : Course 1/4 programme
  1. Optical fibre physics and principles
  The medium
  Principle of communication using light
  Types of fiber optics
  2. Optical fibre Cables
  Cable types, evolution, active systems
  Cables with tubes, ribbons
  3. Optical fibre accessories
  Connectors and splicing optical fibre
  Jumpers between equipments
  Connecting with optical fibre
  4. Installing optical fibre
  Urban zones, other
  Street cabinets, manholes and ducts
  Aerial installation
  Inter-continental cables, submarine

## Slide 5: A bit of history
  End of 19th century
    Using mirrors to direct light
    Conducting light in a water jet
  Optical fibre created in the second half of 20th century
    1961 Elias Snitzer and the theory for single mode fiber
    1973 Bell Laboratories created the first fibre
    1975 first telecommunication network on fibre optics
    1980 Sprint uses the first full fibre optic network
    1991 Desurvire et Payne demonstrate optic amplification, opening the field to long haul communication and internet
  Source

## Slide 6: Optical Fibre A bit of physics Medium characteristics

## Slide 7: Optical Fibre, basic principles
light transmission
  Transmission components
    Coding the message into electric input
    Transcoding the electric input into light signal
  … and the reverse operation
Principle of a wave guide
  Fibres are behaving like a guide for the signal
  Optical physics applies, including
    Reflections
    Refraction
    Attenuation due to the material
Optical Fibre and LASER are combined and optimise signal transmission

## Slide 8: Electromagnetism and transmission
Electromagnetic spectrum
  Large use of the electromagnetic spectrum for technology
Used spectrum for fiber optic
  Using wavelength close to infrared … above visible light
  Wavelength @ 0,85µm + 6 bands
  (see table)
Wave length
Frequency
1nm
Gamma
Rays
X Rays
Ultraviolet
Infrared
Hyper frequencies
Radio waves
1µm
1cm
1m
1km
1EHz
1PHz
1THz
1GHz
1MHz
1kHz
Color | From… | …to
Red | 0,62 - | 0,70 µm
Orange | 0,59 - | 0,62 µm
Yellow | 0,57 - | 0,59 µm
Green | 0,50 - | 0,57 µm
Blue | 0,44 - | 0,50 µm
Violet | 0,40 - | 0,44 µm
 | From… | …to
O | 1,26 - | 1,36 µm
E | 1,36 - | 1,46 µm
S | 1,46 - | 1,53 µm
C | 1,53 - | 1,565 µm
L | 1,565 - | 1,625 µm
U | 1,625 - | 1,675 µm

## Slide 9: Typically used wavelength
Range of wavelength for Optical Fibre
  From 800nm to 1600nm (visible spectrum is from 400 to 700 nm)
  Commonly used wavelength is
    850 nm and 1300 nm for multi-mode fibres
    1310 nm
    1550 nm
  Highly depends on the fibre index in one hand and the availability of laser on the other hand
  These wavelength are optimising transmission properties of the fibre

## Slide 10: LASER technology
What is LASER?
  Light
  Amplification by
  Stimulated
  Emission of
  Radiation
Principle and advantage
  Coherent light
    Constant wavelength
  Spatial coherence that can be focused
    Cutting application
    Focused energy for long distance emission
    Temporal coherence
    Very narrow spectrum (single light color)
    Possibility to emit ultrashort pulses

## Slide 11: Using light for transmission : celerity
Wave physics… Basics about celerity
  Wave characteristics in the fiber defined by its
    Wave length (m)
    Frequency (Hz)
    celerity (m/s)
Medium characteristics
  « i » defines the medium
  Depending on its characteristics,
  celerity and wavelength vary
Small Application
  m
  Propagation between Paris and New-York (~5000 km)
  16,6 ms

## Slide 12: Using light for transmission : refraction
  Refraction
  Variation of direction of a wave propagating from one particular medium to another
When do these phenomenon apply with optical fibre ?
  Refraction
    light entering in a fibre
    Light moving from one fibre to another through a connector
  Reflection
    light reaching the border of the fibre while propagating
    light striking mirror in splitter equipments
  Reflection
  Brutal change of direction of a wave striking a surface
  Absorption
  Transfer of energy while a wave propagated through a medium

## Slide 13: Using light for transmission : refraction
Wave physics… basics about refraction
  Refraction is the ratio between propagation in vacuum conditions and in a specific medium
    refraction value by definition refraction in vaccum or in the air is
    celerity (m/s)
Small Application

## Slide 14: Fibre characteristics
Attenuation
  Related to how the signal is getting weaker
  Linear attenuation corresponds to reduction of signal power based on distance
  Related to the wavelength (due to Rayleigh diffusion on the shorter waves)
  Attenuation can be compensate by amplification systems
Chromatic Dispersion
  Related to signal spreading : signal is getting larger as signal propagation celerity depends on wavelength
  This effect can be compensated by fibre with index profile
Celerity
  Approximately the same than for copper, i.e. 75% of light celerity
  Can be even more in laboratories
  Repeaters on long haul fibres are reducing average speed of the signal
Transmission rate
  The highest rate communication was made by NEC @ 1Pbps (1M Gbps)
Paris – Noumea
20 000 km
theory 90 ms
in practise 280 ms
1 Pbps

## Slide 15: Creating optical fibre
MAterial
  Silicium (SiO2) is the most used material for optical fibre
  Other raw material can be used depending on expected wavelength (longer in IR)
    fluorozirconate, fluoroaluminate, and chalcogenide glasses
    crystalline materials like sapphire
Manufacturing process
  Silicium is melt from some piece in a vapored environment with various chemical vapors, including silicon tetrachloride (SiCl 4 ), germanium tetrachloride (GeCl 4 ), and phosphorous oxychloride (POC1 3 )
  A cylinder of pure silicium is created (10cm long)
  The cylinder is strechted to form the final core fibre.
  This fibre is rounded by a coating made of a different silicium (with a different refraction index including for instance phosphore or germanium).
  The fibre is finally polished to prevent incorrect reflections.

## Slide 16: Optical fibre typical values
The fibre itself
  Core : ~10 µm
  Coating : ~100-150 µm
Cable
  Typical number of fibres in a cable varies depending on the use
    Few fibres for local use in an office or home
    Dozen to few dozen of fibres for collecting trafic or submarine cables
    Hundreed of fibres for backbone / agregation cables
    … some cases of thousands of fibres for datacenter connection (quite often preference is given to multiplying cables rather than concentrating fibres on a single cable)
  Typical cable section : from less than a mm to few cm
  … with a strong impact on the capability to get into existing ducts in dense areas

## Slide 17: Optical Fibre Different types of fibre / cables

## Slide 18: Application of refraction to optical fibre
Principle of wave propagation in Optical Fibre
  Reflexion and refraction are used to guide the signal in the fiber.
  The principle is:
    To cancel any refracted ray
    To maximise the reflexion and therefore to maximise the transmitted signal energy
  To reach that objective, a fiber is made of multiple layers:
    A core made of silicium with a fixed refraction index
    A coating with a lower refraction index
    A jacket to protect the fiber from the outside
  The coating aims at containing the signal within the core of the fiber

## Slide 19: Optical fibre, technology evolution
Optical fibre: single/Monomode
  Reduced size core allowing signal propagation straight
  in the fibre
  One only wavelength at a time, therefore no interference
  Optimized for long haul and capacity
Optical fibre : Multimode
  Multiple waves can coexist
  Attenuation has to be managed over long distances
The other evolution to high rates : Multiplexing and Digital signal management
  EDFA, WDM
  Coherent detection
  Digital Signal processing
Optical fibre in telecommunication is massively single mode fibre

## Slide 20: Limits of refraction for optical fibre
Principle of wave propagation in Optical Fibre
  Reflexion and refraction are used to guide the signal in the fiber.
  The principle is:
    To cancel any refracted ray
    To maximise the reflexion and therefore to maximise the transmitted signal energy
  To reach that objective, a fiber is made of multiple layers:
    A core made of silicium with a fixed refraction index
    A coating with a lower refraction index
    A jacket to protect the fiber from the outside
  The coating aims at containing the signal within the core of the fiber

## Slide 21: Typology of optical fibre
fibre types AND Reasons
  G654 was designed for submarine cables
  G655 an optimisation while WDM was not existing
  G657, G652
  The latter is the evolution of the first, both largely used for terrestrial networks
Notes
  G652 and G657 are very close and can be mixed with some conditions
  G655 was designed originally to maximise rate while multiplexing was not existing
 | G652 | G654 | G655 | G657
Mode | Single mode |  |  | 
Band | Optimal for 1300 nm |  | 0 dispersion @ 1500nm | D, E, S, C, L5
Loss |  | Ultra low loss |  | 
Bending | + |  |  | +++
Typical use | Great for long haul links | Submarine cables |  | Largely used now while applicable for almost any type of use
Optical Fiber lifetime
  Not damaged by light
  The most important risk is environmental conditions (animals, heat/cold, bending…)
  With regards to micro failures (heat/cold).

## Slide 22: Cables to embed and protect fibres
Typical cable values
  Number of fibres embedded
    1 (of few) fibres for jumper cables
    24-48 fo for
      collecting traffic in networks
      Submarine cables
    72/96 for transportation
    144/288 for long haul terrestrial networks / Core networks
    1152++ for specific requirements (for instance between datacenters)
Environmental constraints
  Cables can also embed specific requirements
    LSOH to reduce gaz emission in case of fire
    Increased protection to torsion/bending (however brings a constraint to deployment)
    Specific resistance to animals for instance rats in sewers
  Cables are challenged in datacenters and other sites as people are walking on them…

## Slide 23: Optical fibre, cable technology
Cable with Tubes
  Fibres are gathered in tubes
    Loose tubes
    Micro tubes
Cables with ribbons
  A technology aiming at making easy the connexion of high number of fibres in the same cable

## Slide 24: Cables that brings power
Active Cables … special needs
  To address the need for bringing at the same time communication and power, a typical need for
    Very long haul connection (intercontinental)
    Submarine cables
  Some application also for office building to bring power and telecom facility everywhere in the same cable. Low constraint with electromagnetic fields compared to coaxial cable.

## Slide 25: Optical Fibre Accessories around

## Slide 26: Connectors
Why a (physical) connector ?
  Aligning or coupling fibre
    High precision for the light to get through completely
    Reduce as much as possible loss of energy
  Easy connection/deconnection in an equipement
Characteristics
  Minimum loss (usually around 0,4 dB)
  Reliability and resistance to environmental conditions
  Easy manipulation for connecting devices/equipments
  The most widely used connectors in the area:
  SC (Subscriber Connector), very common
  LC (Lucent Connector), smaller that SC
  FC (Ferrule Connector), used for monomode jumpers, currently replaced by SC connectors
  ST (Straight Tip), used for multimode jumpers, highly résistent to too strong tightening

## Slide 27: Connector history (1/4)
 | Nom long | Norme | Type | Remarque | Illustration
DIN LSA |  | CEI 61754-3 |  | Obsolète | 
EC | European Connector | CEI 1754-8 |  | Telecom | 
FC | Fiber-Ferrule Connector | CEI 61754-13 |  | Telecom | 
ESCON |  |  |  | Mainframe IBM et compatible | 
ST | Straight Tip | CEI 61754-2 | Baïonnette | Développé par AT&T | 

## Slide 28: Connector history (2/4)
 | Nom long | Norme | Type | Remarque | Illustration
LX5 |  | CEI 61754-23 |  | Rarement utilisé | 
LC | Lucent Connector3 | CEI 61754-20 | Snap |  | 
MIC | Media Interface Connector (FDDI) |  |  |  | 
MU |  | CEI 61754-6 |  | Utilisé au Japon | 
OptoClip2 |  | IEC(86B)CFO 10 | Push-pull |  | 
SC | Switching Connector | CEI 61754-4 |  | Standard/Subscriber/Square Connector (Très utilisé) | 
MTRJ | Media Termination - Recommended Jack3 | CEI 61754-18 |  |  | 

## Slide 29: Connector history (3/4)
 | Nom long | Norme | Type | Remarque | Illustration
SMA 905 |  |  |  | Lasers industriels | 
TOSLINK |  |  |  | Audio numérique | 
E-2000 |  | CEI 61754-15 | Snap | Telecom | 
MPO | Multi-fibre Push-On/Push Off | IEC-61754-7; EIA/TIA-604-5 (FOCIS 5) | Snap (couplage multiple push-pull) | Intègre 12 (version la plus courante) ou 24 brins optiques. | 
VFO | Verranne Fibre Optique |  | Vissé | Maximum 2.5GBits/s. | 
Souriau | Souriau 8016 10A 003 |  | Vissé | Multimode. Obsolète. Date des premiers réseaux optiques en France pour la transmission PDH (TNLO 34MBit/s). | 

## Slide 30: Connector history (4/4)
 | Nom long | Norme | Type | Remarque | Illustration
VFO | Verranne Fibre Optique |  | Vissé | Maximum 2.5GBits/s. | 
Souriau | Souriau 8016 10A 003 |  | Vissé | Multimode. Obsolète. Date des premiers réseaux optiques en France pour la transmission PDH (TNLO 34MBit/s). | 

## Slide 31: Connector structure
Fibre cut
  PC – Physical Contact (allow a very low return loss)
  UPC – Ultra PC (even lower return loss)
  APC – Angle PC (the lowest return loss solution, up to 60 dB)
  Depending on the need, conectors can either be mono-fibre or bifibre.

## Slide 32: SFP
Small Form-Factor Pluggable
  This is the optical module that
    Emits the signal on the fibre
    Receives the signal on the other end
    Adapts electric signal to light signal, specific to wavelength
    Includes LED/Laser beam
Different types of SFP according to use
  SFP / SFP+ for various rates (up to 25 Gbps currently)
  Single or bi-fibre adapteur

## Slide 33: Jumpers
Single fibre cables (occasionnaly Bi-Fibre)
  Used for connection between equipement in a rack (also used at home between wall adapter and internet box)
  Allow to (re)map easily connections in datacenters for instance
  SC connector
  LC connector

## Slide 34: Breakouts and half breakouts
Variation on Jumpers
  Allow connection between equipment requiring a set of fibres (typically radio site with multiple sectors)
  Preventing a mess of jumpers between equipments, especially with equipements are not close the one to the others
  Embed connectors, thus imply loss

## Slide 35: Installing optical fibre

## Slide 36: Manholes
Developed infrastructure
  Typically in France GCBLO infra but also other existing partners (Axione…)
  A contract with rules to access the infra
  Number of equipments
  Number of cables
  Access and maintenance
  Some rules for developping infra, especially in dense area depending on cities
Multiple format/size
  L1T/L2T/L3T
  Characteristics, mainly the size and access to ducts
  Interconnection between infra

## Slide 37: Splicing optical fibre
A key for network extension and connections
  Soldering to fibres to offer continuity
Touchy operation
  Aligning the core to avoid refraction/reflection
  Case of G657 and G652
A sensitive operation
  An operator usually made outside
    Sensitivity to dust
    Sensitivity to humity
  …that can lead to signal attenuation
  Targeted attenuation is less that 0,1 dB (usually a challenge)

## Slide 38: Street cabinet
Capability of such cabinets
  Possibility to share space between operators
  Easy access to mapping capability
  Risks of easy access
  Multiple actors from various companies Sometime keys are used… and broken Real difficulty to trace accesses
  Malicious operations, however not that much
Typical use
  FTTH
  Other networks special cases

## Slide 39: Ducts for telecom cables
Existing networks
  Several operators have a duct infrastructure
  Orange has to provide access
  Other existing offers (Axione, Covage, …)
    Constraints in some areas from regulation

## Slide 40: Digging for optical fibre networks
Urban areas
  Existing networks present and prefered when not saturated see previous slides
Suburban and countryside
  Long haul trenches, micro trench made by machines
Rules
  Depth
  Size/Number for ducts normalized
  Soil to fill holes
  Access to manholes and equipment

## Slide 41: Alternative to ducts : aerial net (1)
Already developed network
  Existing networks available for development, for instance in France
    Orange
    Enedis
Constraints
  Type of fibre cables due to resistance between poles
  Some perturbation with vibrations due to wind
  Limitation (weigth and cable capacity) to usually less than 72fo
Risk of the infrastructure
  Weather condition (storms…)
  Malicious acts
  … but much cheaper than digging for ducts, especially

## Slide 42: Alternative to ducts : aerial net (2)
Network from Power Providers
  Existing networks over high voltage lines
  Available for long haul
  Constraints on the places to get in/out the line
    Limited to pole places
    Usually tied to the power provider network
Technologies
  Usually along with a structure cable
  In some case, embeded in the power cable (not usual)
  Due to the structure of the poles, this network is considered as secure as ducts