## Slide 1: Optical Fibre networks 2/4 Multiplexing, coupling, amplifying
Paul JOLIVET
07/10/2024

## Slide 2: Optical Fibre Networks : Course general objective
Get a panorama of Optical Fibre and networks
  Optical Fibre characteristics and advantages
  Technologies around Optical Fibre
  Other components of optical fibre networks
Understand How to design high rates optical fibre networks
  Existing architecture of Optical Fibre networks (FTTH, FTTA, FTTO…)
  Designing a network
  Deployment constraints
Understand High-rate networks trends to future
Notes: Pour reference : https://www.researchgate.net/publication/305181019_Technologie_WDM_en_telecoms_optiques_avancees/link/57842b1208ae37d3af6c1685/download

## Slide 3: Optical Fibre Networks : Course 2/4 programme
  1. Coupling on optical fibre
  Use cases : typically collecting FTTH
  Principle and Technical solutions
  2. Splitting on optical fibre
  Use cases : typically securing signal
  Principle and Technical solutions
  4. Other passive operations
  Modulator
  Attenuation
  Filtering
  Polarisation splitting
  Isolation
  4. Amplifying signal
  Use cases : typically long haul transmission
  Principle
  Technical solutions and constraints
  5. Multiplexing (WDM)
  Use cases : typically optimizing fibre
  Principle
  Various types of WDM, technologies
  Technical solutions and constraints

## Slide 4: Passive and active components
Active components
  Equipment embedding a component that emit light (including laser or LED)
  Typically
    Amplifiers
    Routers
  Active components always require to be powered
Passive components
  Equipment that interfere with the light going through them (propagation, polarisation…)
  Typically
    Splitters
    Couplers
  Passive component do not mandatorily require power supply; however this could be necessary if there is a need for
    monitoring
    configuration
Two types of components
On optical fibre networks

## Slide 5: Coupling signals on optical fibre

## Slide 6: Optical fibre couplers : principles
  Multiplication of the input/output fibres with the same signal
    Allows to emit a single signal from one place to multiple other places
    In some cases multiple signals coming from multiple fibres to one only point
  Optimizing the fibre capacity by using the free space
    Several signals can physically share the fibre capacity
    Principle is here to combine two inputs in a single fibre
  The opposite operation is called splitting. Splitter is used for securing signals, it will be defined afterwards in this course
Coupler terminology can be used to define two similar technical solutions

## Slide 7: Optical fibre couplers : use cases
Optimizing resource
  Several users can share the same resource that they do not need fully
  Typical for FTTH infrastructures
Broadcasting signal
  For systems requiring the same information to be share in multiple equipments (datacenters for instance)
Securing signal
  Making it circulating by multiple ways
  Preventing risk of broken cable
  Doubles the required resource
Drawbacks
  Sharing resource (limiting for the single user)
  Loss of energy while splitting signal
  Attenuation by equipments / connectors

## Slide 8: Coupling optical fibre
The principles
  Sharing the input power between multiple inputs
    Power splitting
    Depending on the used technology, the balance of the power can be adjusted
Technical constraints
  The quality of coupling is related to
    Distance between waveguides
    Length of coupling portion
    Quality of the fibre and connection
The technical implementations
  Transfer by proximity of the waveguides
  Transfer by fusion
    Robust solution
    No component addition
    Require expertise
    Adapted for limited number of coupled fibres
  Transfer in dedicated connectors (limit of the loss)

## Slide 9: Optical couplers : equipment
This can be the story of connectors
  See the picture on the side
  For coupling a limited number of fibres, usually
  With a warning : connectors are adding attenuation to the signal
Typical use : FTTH networks
  On a GPON architecture, up to 128 users’ trafic can be coupled on a single fibre
  Coupling can be made in several steps in the distribution network

## Slide 10: Splitting signal on optical fibre

## Slide 11: Optical fibre splitters : use cases
Broadcasting signal
  Such functionality can be used for instance in datacenters where multiple equipment a redundant to ensure security and shall get the exact same information to duplicate it
Monitoring activity
  Extracting part of the signal (low) to follow-up what is happening on the fibre
Securing signal by making it circulating by multiple ways
  Typically used for FTTA networks based on loops
  An equipment is connected by to ways to the same collection centre (or alternatively by different ways to different collection points). In case one way is damaged, the other is used.
  In the case of one collection point with two identical inputs, a physical switch is used

## Slide 12: Optical fibre splitters : principles
Basic Principle
  Use of a material prism/mirror
    Part of the light goes straight
    Part of the light is reflected
Constraints
  The output signals also split energy with an unbalanced ratio (could be as much as 70/30)
  An existing loss of energy in the operation for passive splitters
    Either the loss of energy is acceptable for the transmission
    Either it is not, in such cases, amplification shall be combined

## Slide 13: Other passive functions on optical fibre

## Slide 14: Modulator
Principle
  Modulating the light signal in the fibre
  Aiming at generating pulses for coding information
  Modulation can be either done
    By modulating the signal prior the laser diod (out of the scope here)
    By modulating light after the laser diod (external modulation)
  External modulation is done by
    interfering with the light (some acoustic systems)
    playing on the refraction on the fibre
Constraints
  Loss of insertion with several dB
  Some of the modulator still require energy to contain the loss of power to its minimum

## Slide 15: Attenuation
Principle
  Reducing signal intensity on the fibre
  Objective is to prevent glare on reception (for short range)
  Could also compensate drift being the result of used components
  Attenuation can be made
    On a fixed value (typically the connector shown aside)
    With a variable value (usually an active component in that case) Variable Optical Attenuator
Technology
  Thermo optic
  Material filtering / Liquid cristal

## Slide 16: Filtering
Principle
  Filtering incident signal
  Prevent “noise” created by distance, unwanted coupling or active component combined with these reasons
  Focus the light signal
  Also used for passive WDM solutions to extract a wavelength
Technology
  Bragg net
  Chromatic filtering
  Polar filtering by use of a set of cristals/prism

## Slide 17: Polarisation splitting
Principle
  A specific type of filter used for separating signals with different polarisation or to compensate the polarisation drift
Technology
  Based on cube prisms
  Use of calcit properties
  The main point is to get parallel propagation direction after the application of the polarisation filter

## Slide 18: Optical isolator
Principle
  A specific type of filter used for allowing only one propagation direction in the fibre
  The main aim is to eliminate parasite reflexions of the signal within the optical fibre
Technology
  Usually based on a Faraday rotator that
    polarize the signal
    optical fibre properties that looses orthogonal propagation
    strongly attenuate the parasite propagations
  The Faraday rotator is based on cristal. Each cristal has a Verdet constant that characterize an absorption to a certain wavelength Typically for telecom optical fibre: Yttrium Iron Garnet
Y3Fe2(FeO4)3

## Slide 19: Optical circulator
Principle
  A component that allows to have several light signal in a single fibre, typically to separate opposite sides propagation
  A solution for bidirectional communication
Technology
  A 3-port approach using
    A Faraday rotator for the signal polarization
    Cristal, used as prisms/mirror
  To reduce interferences in this operation, orthogonal polarization is used commonly in this circulator
  The Faraday rotator is based on cristal. Each cristal has a Verdet constant that characterize an absorption to a certain wavelength Typically for telecom optical fibre: Yttrium Iron Garnet

## Slide 20: Amplifying signal on optical fibre

## Slide 21: Amplifier and regenerator
One objective
  Long distance communication implies attenuation and has limits
  Signal has to be maintained in order to connect distant points (over oceans for instance)
Two principles
  Amplifier
    Signal amplification
  Regenerator
    Signal amplification
    Reshape the signal to prevent distorsions
    Synchronize the signal
  Both components are active as requiring to boost signal energy as a minimum
  The regenerator is a component that is completely adapted to the rate and protocol as getting as deep as reshaping/synchronizing it. It works as a receiver/emitter

## Slide 22: Optical amplifier characteristics
Principle
  Amplification without conversion (i.e. no work on the content itself). It is usually stimulated by a gain medium and doping ions in this structure.
  In some cases additional light is generated to dope the signal. In those cases some parameters can apply to focus amplification
Technical solutions
  Various solutions applicable to optical fibre:
    EDFA
    Semi-conductor optical amplifier
    Raman amplifier
    Optical parametric amplifier
G

## Slide 23: Semi conductor amplification (SOA)
Principle and characteristics
  The gain medium is embedded in a semiconductor
  The pump is powered by electricity
  Semiconductor characteristics
    Anti-reflection coating with a result of less than 0,001%
    Usual semiconductors can operate in the band of 850 and 1600 nm
    Gains can be up to 30dB
Pros and cons of the technology
  Much less expensive than other technical solutions
  Higher noise
  Lower gain
  Risk of non-linearity on the signal

## Slide 24: Raman amplifier
Principle and characteristics
  The basic principle is to create the amplification by a non-linear interaction with the fibre (used as the gain medium) and multiplexing:
  the signal
  a pump laser
  The coupling can be directional, contra-directional or in some cases a combination of the two.
  This also implies filters to compensate the coupling effects on the line
Pros and cons of the technology
  Higher power requirement compared to EDFA
  Can be adjusted in terms of wavelength to the exact need
  Amplification is reasonably flat over the wavelength (note that this could be a serious drawback as this implies amplifying noise as well)

## Slide 25: EDFA amplification
DFA Principle
  The principle is to force the signal through a doped fibre
  The medium is powered by a pump that excites ions in the section of the doped fibre.
  The interaction between those ions and the signal creates the amplification
Characteristics
  Amplification window
    Range of wavelengths
    Spectroscopic properties of the dopant ions
    Structure of the glass matrix of the doped fibre
EDWA (erbium-doped waveguide amplifier)
  DFA amplifier including a waveguide to boost
  Erbium ions are used in the doped fibre (corresponds to the used wavelength between 980 and 1480 nm)

## Slide 26: Multiplexing on optical fibre

## Slide 27: Multiplexing problematic
Optimization of the ressource
  Fibre optic capacity is huge
  The limitation is still on the emitting/receiving equipments
Reality is
  The total demand in terms of capacity is currently doubling every year
  Multiplicity of emitters and receivers
  The expected capacity of each transmission is reasonnably significant
    FTTH sold capacity is about 1-2 Gbps per user, maximum rate
    5G radio site target maximum rate is about 10-25 Gbps
  The largest customers are point to point
The equation is:
  Deploying future proof infrastructures (not adding cables on regular basis)
  Not making bicycles running on motorways, reducing capacity

## Slide 28: Multiplexing technical solutions
Frequency division (Wavelength)
  The frequency band is split into sub-bands, allocated each to a user
  The challenge is to make the best compromise between
  the correct size for the sub-band (vs rate)
  the space between bands to master interferences
Time DIvision
  Time slots are allocated to each users
  Allows to combine multiple low rate messages into a high rate signal
  The limit is the compromise between available rate and real time combination
Code Division
  The principle is to share the whole bandwith and to identify the users by a code signature
  Used a lot in the radiofrequency systems, some trials in the optical world
Combination of solutions
Chart: FDM/WDM
Slot 1 | 1
Slot 2 | 1
Slot 3 | 1
Slot 4 | 1
Slot 5 | 1
Slot 6 | 1
Slot 7 | 1
Slot 8 | 1
frequency
time
Chart: TDM
Band 1 | 1
Band 2 | 1
Band 3 | 1
Band 4 | 1
Band 5 | 1
Band 6 | 1
frequency
time

## Slide 29: Multiplexing light principle
Wavelength Division Multiplexing (WDM)
  The optical fibre bandwidth it split into n carrier bands
  Each band allows communication for a modulated signal
  Some constraints:
  - Space between bands to avoid interferences
  - Total bandwidth (limitations of equipments)
  Note that this is similar to FDD, however, in WDM case, the delta between band is large compared to the wavelength (here approximately 1nm)
Further multiplexing
  In addition to WDM, Time Division Multiplex can apply to each of the emitter/receivers
MUX
λn
λ1
λ2
deMUX
λn
λ2
λ1
Optical Fibre

## Slide 30: Wavelength and multiplexing
Multiplexing sources
  The system used at that time allows up to 64 bands on a fibre which allows typically up to 640 Gbps (with the assumption of the typical 10Gbps channels… to be enhanced)
Technical requirement
  Need for transceivers to adjust the signal to
  Allocation of carrier wave

## Slide 31: WDM technologies : DWDM
Dense Wavelength Division Multiplexing
  Principle is that technology is called dense as soon as the space between bands is lower than approximately 1nm
  Up to 160 wavelength on the same fibre
  Space between wavelength is typically:
    either 0,2nm (corresponds to 25GHz), i.e. 160 bands
    or 0,4nm (corresponds to 50GHz), i.e. 80 bands
  Implies electronics to regulate laser temperature
Typical use
  A costly technology compared to other WDM implementations
  Preferably used for long haul connections (typically submarine cables)
  Dedicated to point to point connections
A variation of DWDM : U-DWDM (ultra dense)
  Bands space at 0,08nm, up to 400 channels available

## Slide 32: WDM technologies : CWDM
Coarse Wavelength Division Multiplexing
  Wavelength are spaced by a guard of 20nm
  Allows up to 18 channels on the same fibre
Typical use
  Cheaper than DWDM but optimizing less the resource
  Used a lot for terrestrial communication
  Local
  Metropolitan
  Applicable to
A variation of DWDM : WWDM (Wide)
  Only 4 channels are allowed

## Slide 33: WDM Fibre optic networks topology
Coarse Wavelength Division Multiplexing
  Wavelength are spaced by a guard of 20nm
  Allows up to 18 channels on the same fibre