## Slide 1: Optical Fibre networks 3/4 Network topologies
Paul JOLIVET
02 dec 2024

## Slide 2: Optical Fibre Networks : Course general objective
Get a panorama of Optical Fibre and networks
  Optical Fibre characteristics and advantages
  Technologies around Optical Fibre
  Other components of optical fibre networks
Understand How to design high rates optical fibre networks
  Existing architecture of Optical Fibre networks (FTTH, FTTA, FTTO…)
  Designing a network
  Deployment constraints
Understand High rate networks trends to future
Notes: Pour reference : https://www.researchgate.net/publication/305181019_Technologie_WDM_en_telecoms_optiques_avancees/link/57842b1208ae37d3af6c1685/download

## Slide 3: Optical Fibre Networks : Course 3/4 programme
  1. Topologies for Fibre network
  The requirement, the constraints
  Applicable solutions
  2. Submarine/Intercontinental
  Use cases : typically securing signal
  Principle and Technical solutions
  3. FTTH
  GPON architecture
  Equipments
  Technical solutions (coupling)
  4. FTTA
  Evolutive architecture
  Urban areas and loop architecture
  Countryside and logical loops
  Equipments

## Slide 4: Network topologies

## Slide 5: Choosing a network topology
The need
  High rate transfers (but how much?)
  Security
  Reliability
    Trafic continuity whatever is broken
    High rate with limited loss
  Latency (for accessing services)
  Distance/Coverage
Solutions
  P2P, dark fibre allocation
  Tree
  Loops

## Slide 6: Network access through telecommunication networks

## Slide 7: Network/Internet Acces
Mean/resource giving an user the capability to access network services (Internet, Intranet, service plateforms)
Accès mobile :
1G/2G/3G/4G/5G
Wimax, etc.
Accès fixe :
RTC, RNIS
xDSL
DOCSIS
FTTH/GPON
Le Modem acoustique
Vitesse théorique de 300 bauds (~300bps)

## Slide 8: A bit of history
RTC/PSTN : local phone loop + phone call
Modem dialling a number related to a NAS (Network Access Server)
The communication is a phone call
Baud rate limited to modem capability (V.92  56kbps)
RNIS/ISDN :
Digitalizing (copper) local loop
2x64kbps + 16kbps (2B+D)
E1/T1 :
2Mbps and more
used in preference to connect central offices together
xDSL : Based on the copper pair but not the telephone network itself
DSLAM
Several types (ADSL,VDSL, SDSL, etc.)

## Slide 9: Network access using copper lines
Central Office
Home
@
RTC
NAS
Modem
56k

## Slide 10: Towards the end of copper lines
Notes: Gain pour Bouygues Télécom : réduction de l’OPEX
Avantages en général : plus d’entretien du cuivre, libération d’espace (NRA, génie civil)

## Slide 11: Using coaxial link for the access
DOCSIS (Data Over Cable Service Interface Specification)
2 box chez Bouygues Telecom :
- OB1-C (samsung)
- GALGAL 3784B (SAGEM)
CMTS
modem
HFC
modem
modem
Hybrid Fibre Coaxial network
eCMTS :
~OLT +
~ONT/CMTS
Notes: E : extended
CMTS + eCMTS (en vrai OLT + ONT/CMTS)

## Slide 12: Using coaxial link for the access
DOCSIS | Année | Débit | Apports | QAM
1.0 | 1997 | 5/40 Mbps | TDMA | 16
1.1 | 1999 | 10/40 Mbps | TDMA | 16
2.0 | 2002 | 30/40Mbps | +S-CDMA | 64
3.0 | 2006 | 30/1000Mbps | +S-CDMA / IPv6 | 128/256
3.1 | 2013 | 2/10Gbps | +OFDM/OFDMA | 4096
4.0 | 2017 | 10/10Gbps - 40/40 (10/6 en pratique) | +OFDMA+ | 8192
DOCSIS® 4.0 Technology - CableLabs

## Slide 13: FTTx, access on optical fibre
And also : FTTS (street), FTTN (Neighbourhood), FTTE (Entreprise), …
FTTR (Room), a chinese manufacturer on the project. The principle is to use optical fibre within the local network to enable very high speed connection.
FTTN
FTTdP
FTTH
FTTLA / FTTB
FTTC
FTTCab
FTTO
FTTA
Notes: FTTC : Fiber to the Curb  PC/DSLAM ou coax
FTTN :  SR / DSLAM (ou coax ?) – monté en débit
FTTB = FTTLA intérieur - coax
Revoir les définitions :

## Slide 14: FTTH network architecture

## Slide 15: FTTH, Internet access at home
Fiber networks to deliver internat at the Home
  Several systems were tested depending on deployment constraints
    Fiber To The Home (FTTH)
    For the history, systems offering the last hop based on coaxial cable or sometimes even copper line
      Fiber To The Last amplifier (FTTLa) / FTTN (Fiber To The Neighborhood)
      Fiber To The … Node / Curb / … (variable according to distance)
      Fiber To The Building (FTTB)
  Some rate limitations on the last hop, however much more than xDSL
  An optical fibre network anyways underneath
Characteristics of the network
  Optical fibre core
  PON architecture for the network
  End connection on an operator box

## Slide 16: FTTH passive network architecture
PMI = Point de Mutualisation Immeuble
PME = Point de Mutualisation Extérieur
PBO = Point de Branchement Optique
PTO = Point de Terminaison Optique
PD
NRO
Tête de
câble
PA
PME
PBO
PTO
Colonne
rampante
PA
PMI
PBO
PTO
Colonne
montante
NRO = Nœud de Raccordement Optique
PD = Point de Distribution
PA = Point de Adduction
Périmètre de l’opérateur de mutualisation
Périmètre de l’opérateur commercial
Transport *
Distribution
Adduction
Colonne montante
ou
Colonne rampante
Branchement
NRO
Point de
Mutualisation (PM)
Point
d’adduction (PA)
Point de
Distribution (PD)
Point de
Branchement
Optique (PBO)
Tête de
câble
Point de
Terminaison
Optique (PTO)
Immeuble ou zone mutualisée
Logement

## Slide 17: Network in high density areas Single fibre mutualized
PoP
PoP
PoP

PoP
Information :
Free Infrastructure
Orange
Bouygues Telecom
SFR


Mutualisation point
Horizontal : 4 networks
Vertical : monofibre mutualised

Shared fibre : Bouygues Telecom, Orange, FREE et SFR
Brassage
Operator CO
Point of Presence for an operator
PoP
Coupler
1 fibre par logement partagée entre ensemble des OC
OLT

## Slide 18: Network in medium density areas Single fibre mutualised
PoP
PoP
PoP

PoP


Horizontal : 4 déploiements
Vertical : monofibre mutualisé

Les NRO des OC
OLT
PM
1
2
PRDM
PM
PM
PM
PM
1 fibre par logement partagée entre ensemble des OC
Cas 1: PM < 1000 lignes
Offre de raccordement distant doit être proposée par l’OI raccordant les logements au PM.
Le Point de Raccordement Distant Mutualisé (PRDM) doit regrouper au 1000 lignes.
L’OI propose aux OC des liens entre le PRDM et les PM.
Cas 2 : PM > 1000 lignes
L’OI n’a pas l’obligation de proposée une offre de raccordement distant.
Le PM doit contenir au moins 1000 lignes.

## Slide 19: FTTH - PON vs P2P access
Uplink ethernet (shared)
Shared fibre
Dedicated fibre
PON :
1 port = 1 fibre = 64/128/256 customers
P2P :
1 port = 1 or 2 fibres = 1 customer
Splitters 1 to n

## Slide 20: FTTH - PON vs P2P upstream
Uplink ethernet partagé
Fibre partagée
Fibre(s) dédiée
PON :
Upstream : x flux unicasts
P2P :
1 seul flux up et down

## Slide 21: FTTH - PON vs P2P downstream
Uplink ethernet partagé
Fibre(s) dédiée
PON :
downstream : 1 seul flux chiffré
P2P :
1 seul flux up et down
Fibre partagée
ONT
ONT
ONT
ONT

## Slide 22: PON Tree elements
ONT : Optical Network Terminaison
ONU : Optical Network UNIT
1 ONT is a mono user ONU
ODN : Optical Distribution Network / PON tree
Olt : Optical Line Termination
amont
aval

## Slide 23: PON Variations
 |  | Rate (downlink) | Rate (uplink) | reference | Comment
B-PON | Broadband-PON | 1 Gbps | 622 Mbps | ITU-G.983 | 
A-PON | ATM-PON |  |  |  | Almost not used
E-PON | Ethernet-PON | 1 Gbps | 1 Gbps | IEEE 802.3ah | Based on Ethernet
G-PON | Gigabit-PON | 2 Gbps | 2 Gbps | ITU-G.984 | To replace B-PON No full backward compatibility however Supports various protocols
A metropolitan network architecture
  Corresponds to levels 1-2 in the OSI network architecture
  Developed for high rate internet networks
  Supports usually both IP and ATM (secondary)
An architecture that evolved
  Several solutions were developed

## Slide 24: APON / BPON
APON : ATM PON - 1999
BPON : Broadband PON / includes APON
Based on G.983 series
Rates :
155/622 mbps down / 155mbps en up (APON)
1,2 Gbps down / 622mbps en UP (BPON)
Wavelength APON :
Upstream : 1260-1360 nm
Downstream : 1480- 1580 nm (1 fibre) 1260-1360 (2 fibres)
G983.1
G983.2
G983.3
G983.4
G983.5

## Slide 25: GPON
Gigabit PON
Basé sur la famille de normes G.984
TDM
Débit :
Downstream 2488,32
upstream 1244,16 (max 2488,32)
Longueurs d’onde :
1310 nm (upstream)
1490 nm (downstream)
Note : diplex-monofibre
(mode bifibre prévu par la norme)
G984.1 - General characteristics
G983.2 - physical media dependent (PMD) layer specification
G983.3 - Transmission convergence layer specification
G983.4 / G988 - ONT management and control interface specification
G983.5 - Enhancement band

## Slide 26: XG(S)PON
X (Symetric) Gigabit PON
Basé sur les familles de normes
G.987 (XG)
G.9807 (XGS)
2,5/10G (XGPON)
10Gbps bidirectionnel (XGSPON)
- 1277 nm upstream
- 1570 nm downstream
XGPON
G987.1 - General requirements
G987.2 - Physical media dependent (PMD) layer specification
G987.3 - Transmission convergence (TC) layer specification
XGSPON
G9807.1 - 10-Gigabit-capable symmetric passive optical network (XGS-PON)
G9807.2 - Reach extension

## Slide 27: NGPON2
Next Generation PON 2
Basé sur la famille de normes G.989
TWDM
Débits :
4x10G (Opt. 8x10G)
Longueur d’onde :
Downstream 1596-1603 nm
Upstream :
- Wideband option 1524-1544 nm
- Reduced band option 1528-1540 nm
- Narrow band option 1532-1540 nm
G989.1 : Réseaux optiques passifs de 40 gigabits (NG-PON2): Caractéristiques générales
G989.2 : Réseaux optiques passifs de 40 gigabits - version 2 (NG-PON2) : Spécification de la couche dépendante du support physique (PMD)
G989.3 : Réseaux optiques passifs de 40 gigabits (NG-PON2): Spécification de la couche de convergence de transmission

## Slide 28: 25GPON
  Basé sur la norme IEEE 802.3ca et une extension du XGS-PON pour la couche de convergence
  25GSPON servirait d’intermédiaire entre le 10GPON et le 50GPON
  25G symmetric PON multi-source agreement (25GS-PON MSA)  10+ constructeurs
  Débits :
  25/10 Gbps
  25/25 Gbps
  Longueurs d’onde :
    Prise en compte de plusieurs options de longueur d’onde upstream
                UW0 : 1270nm – collision avec le XGSPON
                UW1 : 1310nm – collision avec le GPON
                UW3 : 1286nm – pas de collision  permet la coexistence GPON / XGSPON / 25GPON
  En downstream :
      1358nm
Notes: GAP technologique moins important par rapport au 50 GPON
Differences
Rate : 24,8832 Gbit/s
Structure de frame de 125 us conservée
Blocs de 40 octets
+1 Alloc-IDs +1 ONU-Ids pour les 25G ONUs
LDPC FEC
Rate : 24,8832 Gbit/s
        Source :
              https://www.25gspon-msa.org/
              25GS-PON-Specification-V2.0

## Slide 29: 50GPON
Higher Speed Passive optical networks
Basé sur la famille de normes G.9804
Débits :
50/50 Gbps
50/25 Gbps – 50/12,5 Gbps – 50/10 Gbps
Longueurs d’onde :
Downstream : 1340– 1344 nm
Upstream : compatibilité avec 10gbps and 25gbps +
1290 nm~1310nm : ne peut coexister avec le GPON US (1310 nm)
Ou
1270~1280 nm : ne peut coexister avec le 10GPON US (1270 nm)
ou
~1286 nm : coexistence possible avec GPON et XGSPON
G.9804.1 – requirements
G.9804.2 - common transmission convergence layer specification
G.9804.3 - physical media dependent (PMD) layer specification
G.Hsp.50gpmd
Notes: Nécessite un gap technologie, notamment au niveau des composants, bien plus important

## Slide 30: 100G PON
Tests réalisés (nokia + vodafone) – annoncé en février 2021
1 seul lambda
Téléportation virtuelle ?
3D holographique ?
5G/6G
https://www.nokia.com/about-us/news/releases/2021/02/02/nokia-and-vodafone-showcase-record-breaking-100-gigabit-fiber-broadband/

## Slide 31: EPON/10GEPON/50GEPON
1G EPON - 802.3ah (2004)
1/1 Gbps
10G EPON - 802.3av (2009)
  10/1 Gbps
  10/10 Gbps
  freebox delta (commercial : 8Gbps/700Mbps)
50G EPON - 802.3ca (2020)
  25/10 Gbps
  25/25 Gbps
  50/10 Gbps
  50/25 Gbps
  50/50 Gbps

## Slide 32
Etat des lieux
GPON
G.984.x
EPON
802.ah
XGSPON G.9807.x
10G-EPON
802.av
NGPON-2
G.989.x
100G
50G
25G
10G
1G
25GPON
MSA
50GPON
G9804.x
100GPON / 200GPON / TERAPON
25G/50G-EPON
802.ca
2003
2004
2009
2013
2016
2020
2021
202x / 203x
IEEE
IUT-T
Hybride
TbD
Majoritairement déployé dans le monde
Solutions choisies par certains opérateurs
Solution choisie par la plupart des opérateurs
Solution proposée par certains constructeurs (Nokia, DZS, etc.)
Tous les constructeurs travaillent dessus
Solution coûteuse, peu utilisée
32

## Slide 33: PON Characteristics (1/2)
Passive Optical Network (PON)
  A network architecture based
    Optical fibre
    Sharing resource by using massively couplers (possibility to have a 2-level coupling structure), still possibility for passive P2P (see FTTO later on)
  A connection between
    an Optical Line Termination (OLT) that gives access to network and service
    an Optical Network Termination (ONT) that is the connection point for the end user (Optical Network Unit in the case of FTTB/FTTLa)
Optical fibre characteristics
  Single-mode Fibre (the usual case) with typically G657 in Europe
  Bi-directional communication on the fibre (downlink 1490 nm, uplink 1310 nm)
  Couplers to access the network resource
  TDMA multiplexing of users in both directions of transmission

## Slide 34: PON Characteristics (2/2)
Security
  A requirement especially on a shared network
  End to end AES128 coding
Coupling limits
  Resource sharing on FTTH is a compromise between
    Optimizing the investment over an optical fibre network
    Providing significant resource to the end users
  A common value for fibre coupling is 1/64, it however can reach 1/128 in some places.
Limits
  Distance is limited to ~20 km max mainly due to
    Laser beam used
    Massive use of couplers/splitters on the line

## Slide 35: PON Components
Passive Optical Network (PON)
  A network architecture based
    Optical fibre
    Sharing resource by using massively couplers (possibility to have a 2-level coupling structure)
  A connection between
    an Optical Line Termination (OLT) that gives access to network and service
    an Optical Network Termination (ONT) that is the connection point for the end user (Optical Network Unit in the case of FTTB/FTTLa)
Optical fibre characteristics
  Single-mode Fibre (the usual case) with typically G657 in Europe
  Bi-directional communication on the fibre
  Couplers to access the network resource

## Slide 36: Central Office (NRO)
An anchoring site
  A massive number of end-users connected (several dozen of thousand users)
Optical Line Terminal (OLT)
  OLT, similar to DSLAM in the xDSL terminology
  A set of end-users connection point to transportation network
  Main characteristic :
    Entry point to optical network
    Connected to routers
    Connected to backbone
    Include passive splitters
  In French…
  NRA (Noeud de Racco. Abonné) : xDSL
  NRO (Noeud de Racco Optique) : Fibre

## Slide 37: Central Office / Network sharing
Option 1 : Operators have their own OLT
  The main option : in France most of the Central Office were deployed by Orange and SFR (co construction operations)
  Competition Operators have identified fibres connected to their OLTs through local operator. The traffic is then sent to the end-user operator backbone.
Option 2 : Active Backhaul
  The typical option for low density areas where deployment is not made by operators, but local authorities.
  Happens in some cases for special areas.
  The traffic is routed by the local operator to the end user’s operator connection point

## Slide 38: Mutualisation points (PM)
Equipment that allows mutualisation of Fibre
  The merging point of end-users connection
Several types of mutualisation points
  Indoor for the case of large buildings
  Outdoor
    when houses are connected
    for mutualisation over a full area/district

## Slide 39: Middle connection points (PBO)
Intermediate points between site and end-users
  The merging point of end-users connections
  Typically used in residential areas where multiple connections cannot be done within a building
Characteristics
  A box that allows a set of connections (usually up to 12)
  Access to a cable that is connected to a mutualisation point
  Usually no couplers in such boxes although not forbidden as a rule

## Slide 40: End connection points (ONT)
Optical Network Termination (ONT)
  The end point for end-users connections
  The final optical point : afterwards connection is based on another medium, usually ethernet, could be coaxial (FTTLa)
Characteristics
  Adaptation of transmission medium : optical to electrical
  Similar to a SFP, likely to be replaced by SFP ultimately
  The main difference is the power to supply to ONT
  Some security concerns with regards to ONT
    could be hacked if not located in the final office or appartement
    whereas SFP is by definition located in the delivery point

## Slide 41: How does fibre comes to home ?
The story of an installation
  Network Cable installed
    Using when possible Orange ducts infrastructure
    Digging when required
    Installing a cable in every street from the collecting point
An article in French @ https://www.01net.com/actualites/comment-la-fibre-optique-arrive-jusqu-a-chez-vous-1300062.html

## Slide 42: FTTH in France (1/2)
State of the art
  Most of the country can be connected throughout multiple combination of infrastructures
  4 main operators for end-users
  Multiple local operators for low density areas
A ruled market
  Being an operator comes with commitment to deploy network (coverage, technology, rate…)
  On shared areas, operator commit to provide access to competition in a fair manner
Some resource on @ https://cartefibre.arcep.fr/index.html?lng=3&lat=46.57692011118078&zoom=6.491853096329674&mode=normal&legende=true&filter=true&trimestre=2022T3

## Slide 43: FTTH in France (2/2) : various areas
  High density areas
    All operators have infrastructure
    Sharing verticality of users buildings
  “AMII”/”AMEL” areas
    One operator have infrastructure
      Commitment for coverage and access to competition
      Infrastructure compatible with competition rules
      Capability to host OLT from other operators for their user’s backhaul
    Competition operators are renting fibres
  “RIP”, the “DSP” areas
    Low density areas where RoI is difficult
    Local administration delegates local operator to deploy infra
    Main Operators are dealing with local operator to backhaul customers
      Either by adding an OLT in the Central Office
      Or by negotiating active backhaul
Notes: https://www.maire-info.com/numerique/ftth-rip-amii...-le-lexique-pour-(enfin)-tout-comprendre-aux-enjeux-du-tres-haut-debit-article-23559

## Slide 44: FTTH zones in France
Medium density zones
33,6 M places – 34 700 cities
Private zones
« AMII »
15,9 M places
4 300 cities
63% houses | 37% Flats
Orange
12,9 Mloc.
(81%)
SFR
3 Mloc.
(19%)
Public zones
« RIP »
16,2 M places
27 800 cities
95% houses | 5% flats
High density area
ZTD
7,9 M places
106 Cities
(148 with districts)
High density zones
81%
6,7 M places
Low density zones
15%
1,2 M places
Collectivité Territoriales
Via Délégataires de Services Publics :
Axione, Altitude, SFR Coll., Orange Coll., TDF, SIEA, autres régies
Spec. zones
4%
0,3 M places
Private zones
« AMEL »
1,5 M places
2 600 Communes
95% houses | 5% flats
Orange
0,4 Mloc.
(27%)
SFR
0,8 Mloc.
(53%)
Altitude
& TDF
0,3 Mloc.
(20%)
ZSP = Zone Spécifique
AMII = Appel à Manifestation d’Intention d’Investissement
AMEL = Appel à Manifestation d’Engagement Local
RIP = Réseaux d’Initiative Publique
Notes: Les zones conventionnées (AMII, AMEL)
  Les opérateurs privés s’engagent à déployer la fibre optique, ils signent des conventions avec l’état et les collectivités territoriales.
  Des obligations de couverture sont définies, par exemple 92% des Locaux Raccordables en fin 2020 en AMII.
  Ces zones concernent 55% de la population et représentent un investissement de 6 à 7 milliards d’euros.
Les zones non conventionnées (RIP)
  En dehors des zones conventionnées, les collectivités territoriales déploient des réseaux d’initiative publique (RIP).
  Ces zones concernent 45% de la population et représentent un investissement de 13 à 14 milliards d’euros.
  AMII  initiatives privées
  AMEL  initiatives publiques (Appel d’offre)
  RIP  zones non rentables pour OI, à la charge de collectivités / DSP

## Slide 45: FTTA, from Fiber To The Antenna to Fiber To The Access

## Slide 46: FTTA (Antenna or Access?)
Initially
  FTTA is defined is an optical fibre network to reach mobile networks radio sites
The need
  Increasing rate need for 4G (even more with 5G)
  Latency requirement for 5G services (few ms)
  Security and reliability (even more than for end-user’s internet cx)
The existing solutions
  Optical fibre for transportation
  Backhaul sometimes with optical fibre but wireless beams are used
FTTA first targets radio networks
  Radio site are first priority in terms of requirement
  To have a return on investment, FTTA is also used to collect traffic from other services, including FTTH users in some places, FTTO, …

## Slide 47: Fronthaul or Backhaul principles
Radio site architecture principle
  Antenna(s)
  Remote Radio Head (RRH)
  BaseBand Unit (BBU)
  + energy…
Two solutions for collecting radio
  Backhaul
    Autonomous radio sites
  Fronthaul
    Antenna and RRU co-located
    BBU as part of the anchoring sites
    Connection between RRU and BBU on a dedicated optical fibre per connection usually based on eCPRI protocol
RRH
BBU
RRH
BBU
Rou-ter
network
RRH
BBU
Rou-ter
network

## Slide 48: Fronthaul or Backhaul strategy
Interest of the solution
  Part of a trend for network virtualisation
  Reduces the need for routing and multiplexing technologies
  Focusses site development on a set of datacenters (with the constraint of latency)
Realism plays against fronthaul
  Criticity of optical fibre ressources in dense areas
    Ducts are full
    Buildings owner are reluctant to cables installation (although interested in renting their roof
  Multiplication of large anchoring sites
    (let say… datacenters) in a period where operators are challenged by public on their footprint
    difficulty to identify appropriate sites in dense areas
  Challenges include
    the synchronization of the network
RRH
BBU
RRH
BBU
RRH
BBU
2G, 3G
4G
5G
Rou-ter
RRH
BBU
RRH
BBU
RRH
BBU
2G, 3G
4G
5G
Rou-ter

## Slide 49: FTTA basic needs for operators
Specific requirements
  Large coverage network (4G/5G radio sites will be numerous)
  FTTH density is not required and would have a high cost
  Avoid couplers
Adaptation to urban areas
  A ideal solution (loops, see later on)
  Specific solution to reach areas around
    Railways
    Special zones (commercial zones, airports…)
    Infrastructures (ducts) saturation
    Local rules to dig
Adaptation to Countryside
  Loops are difficult to deploy
  Specific solution to reach areas around
    Motorways
    Private properties (fields, properties aside roads…)
    Topography difficulties

## Slide 50: FTTA Architecture basics
A network architecture based
  Optical fibre loops
  Fibre can be shared by logical means, no coupling
    Use of routers
    Use of splitters and switches for some connection
  A connection between
    The equipment to connect one side
      Radio site
      FTTO customer
      FTTH anchoring site (NRO…)
    The anchoring site (see next slide for more details)
Optical fibre characteristics
  Single-mode Fibre (the usual case) with typically G657 in Europe
  Bi-directional communication on the fibre (downlink 1490 nm, uplink 1310 nm)

## Slide 51: FTTA topology/characteristics
The usual loop based topology in urban areas
  Access to the network always offer two ways to reach anchor site
  Depending on the requirement such possibility is used or not (typically it is for radio sites or FTTH zones, not for FTTO unless special offer)
The material
  Optical fibre typically G657 (for dense areas)
    288 fo for transportation level
    72 fo for distribution or pendulars
    24 for sites abductions

## Slide 52: FTTA topology/characteristics
Logical loops topology for country side
  Loops would be costful and useless on long haul connections
  No physical loops however, keep the loop mind
    Logical loop by using IP routing
    Physical loop by using long haul connections for transportation network (constraints however on latency)
  Importance of sizing and functional split of the anchoring points
  Similar material than for loops
MO
NRA
NRA
Lien inter UU
DN
SO
Amplification
CO
MO
SO
Régénération

## Slide 53: FTTA architecture in layers
  FTTA : Collecting sites
  Network elements connection on loops and intercity links, typically :
    Mobile network (radio sites, Merging points)
    NRA/O, FTTO
    Other connections, hosting capability
CO
CO
MO
SO
MO
CO
MO
CO
MO
MO
SO
MO
CO
MO
CO
MO
Urban area
MO
Urban area
SO
  FTTA : Transportation layer
  Network routing between anchors
    Interloops links and loops
    Intercity (inc. amplification)
    Dark fiber access
  FTTA : Backbone / Core
  Trafic routing within the network
  FTTA, optical fibre and anchoring sites into 3 layers

## Slide 54: A national coverage example
A combination of loops and links
  A set of loops in the main cities
  A set of intercity links to connect them all
The quality of FTTA design
  Setting the correct number of anchoring points
  Covering the areas with high potential of sites to connect
  Offering the possibility to create loops between the cities to secure the connections even though some links would be broken
  Providing opportunities for future extension by
    Adding loops in dedicated areas (cities not addressed at first)
    Adding links to make the network even more dense
    Connecting other types of network on interconnection gates

## Slide 55: FTTA anchoring sites
Small Office
  Also called ILA for some operators
  Main operation is to amplify the signal over long haul link (no SO on dense areas)
Metropolitan Offices
  Sites mainly focus on collection and transportation requirement
  Mainly located on loops of dense areas (inc. cities and places where collecting traffic is required)
  Embed
    Collecting equipements
    WDM equipments for aggregation and transportation
Central offices
  All that a MO is offering
  Additionally the offer services and core network access
  Highly secure sites (some are of vital importance for the overall network)
  Secure by split between different and isolated parts of a building

## Slide 56: Long haul connections and submarine cables

## Slide 57: Long haul connections, the need
The need
  Security
  Latency
Solutions
  P2P
  Tree
  Loops

## Slide 58: Very long haul connections
https://www.submarinecablemap.com/

## Slide 59: A bit of history
The need
  Mainly related to telecommunications and to connect continents
  At this stage, for cost and efficiency reasons, 99% of the communications are using this type of cables
Submarine / Intercontinental cables
  For power and telecommunications in three steps
    Copper cables since 1850
      A cable from France to UK
      England to Ireland
      Corsica to Algeria (Napoleon III)
      Ireland to Canada (1858)
    Coaxial cables since 1956
    Optical fibre since 1988

## Slide 60: Special characteristics cables
Reliable cable
  Rigidity to prevent torsion/bending
  Protection to environment (animals, meteo phenomena, fishing boats…)
  Power can be embedded in the cable itself
Equipments on the way
  The need for amplification on the way due to the distance
  Active systems to be powered
Possibility to add connections/Maintenance
  For maintenance or exceptional diversion, cable can be removed from water
  Typical case of Mediterranean cables getting along the coast waiting to be extended (to Corsica for instance)

## Slide 61: Optical fibre on top of Power Grids

## Slide 62: FTTE and FTTO Services over Optical Fibre

## Slide 63: FTTO/FTTE services
The requirement
  A peer to peer connection
  A fibre is aligned end to end, the operator provides equipment both sides and possibly multiplexed over the distance
Services rather than network
  Three solutions to offer FTTO/E
    Dedicated cable to reach operator network
    FTTH when coverage is compatible
    FTTA when coverage is compatible
  The supporting network provide specific advantages
    Physical security is easy to propose on FTTA loops
    FTTH offer the P2P connection and density on its coverage which means a cheap deployment

## Slide 64: FTTO/FTTE coverage
An offer available where optical fibre are
  A combination of
    FTTH
    FTTA
  FTTH brings the coverage in dense areas (cities…)
  FTTA has a larger coverage, however usually requires some deployment to reach the connection point
Intersection with the wholesale
  Companies are willing to access the internet
  They also usually have requirement for the connection to datacenters
  FTTO service is possibly combined for the operators with dark fibre offers