## Slide 1: Systems Architecture Training Module
C.E.S.A.M.E.S. Institut
Architecture & Systems Engineering On-the-job Training
Week 1/ Day 2
Version 2 – conforme ASE 2022

## Slide 2: course agenda
Introduction
Systems architecture key concepts & framework
Operational architecture and needs engineering
Requirements engineering
Functional architecture
1
2
3
4
5

## Slide 3: Joint work between designers, geometric and EE representatives
2
System designer
Geometric designer
EE designer
Produces an architecture of the system
That helps refining the requirements
That helps allocating the functions to sub-systems
Function
Function
Function
Function
Function
Sub-system
Sub-system
Sub-system
Sub-system
Sub-system
Allocation
Requirement
Requirement
Requirement
Requirement
Requirement
Requirement
Requirement
Breakdown
Breakdown
Helps the system designer for geometry related elements
Helps the system designer for control related elements
At vehicle level, sub-system level 1 or sub-system level 2
RAMS designer
Helps the system designer for RAMS related elements

## Slide 4: course agenda
Introduction
Systems architecture key concepts & framework
Operational architecture and needs engineering
Requirements engineering
Functional architecture
1
2
3
4
5

## Slide 5: Overview of operational architecture
3
The object under analysis:
  The system environment and its constitutive external systems. Each external system belonging to the environment is generally embodied by a stakeholder.
The mission of operational architecture:
  Understanding all expected interactions between a system and the external systems in its environment,
  Specifying the expected lifecycle phases and associated use cases.
The traditional objectives of operational architecture:
  Guarantee a reasonable level of completeness in the identification of needs and organise the methods & the support tools of the repository of needs thanks to knowledge of the environment,
  Provide entry points for the functional architecture work as a result of analysis of the operational scenarios associated with the different use cases of a system that describe all of its external interactions.

## Slide 6: Course agenda
Introduction
Systems architecture key concepts & framework
Operational architecture and needs engineering
  3.1 – Environment architecture
  3.2 – Lifecycle definition
  3.3 – Needs architecture & allocation
  3.4 – Use case analysis
Requirements engineering
Functional architecture
1
2
3
4
5

## Slide 7: Environment architecture concept Maximal systemic perimeter
3
System of interest
environment
Law
Suppliers
Competition
End-users
Customers
Infrastructures
Maintenance systems
Climate
Project system
Technology
Porter forces
Other organiational systems
External interface
Information
Système
Energy
Data
Needs
Maximal systemic perimeter
An example of a generic maximal systemic perimeter of a system. Setting boundaries to the environment of a system should be one of the first architecture tasks.
Humanware subsystems
Software subsystems
Hardware subsystems
Other technical systems
Relation, influence, interface, interaction

## Slide 8: Beware: avoid confusing product system and project system
3
Project system
Product system
Status
Execution actions
Affect
Work on
Implement
Achieve
Function
Function
Sub-system
Sub-system
Project activity
Project activity
Constructional vision
Functional vision
The project system can be seen as a set of actors or activities improving the maturity of the different architectural layers of the product system.

## Slide 9: Environment architecture process overview
3
Identify maximal systemic perimeter
Maximal systemic perimeter
Step 1
Identify the system outside
Step 2
Elimination of non-relevant stakeholders
Organize hierarchically external systems
Step 3
Stakeholders hierarchy
Identify external interfaces
Step 4
Identification of flows and exchanges with the outside
Specify external interfaces
Step 5
The main phases of the system environment architecture process

## Slide 10: Key deliverables of the environment architecture process
3
The two key deliverables of the system environment architecture process are external systems hierarchical map and target system external interfaces identification
External systems hierarchy
Environment diagram

## Slide 11: Environment architecture – Step 1: identify maximal systemic perimeter (1/2)
3
A classical method of exhaustive external systems identification:
the 6 « W » method (Why, What, HoW, Where, When, Who)

## Slide 12: Environment architecture – Step 1: identify maximal systemic perimeter (2/2)
3
External systems list identification
Brainstorming, creativity meetings, etc.
Documentation analyses
Documentation
« tagging»
« 6 W » method in practice: explore system outside through creativity meetings, brainstorming sessions , documentation analyses, interviews, etc. In case of a component design, the vehicle environment diagram and the components architecture of the vehicle are also major inputs sources

## Slide 13: Environment architecture – Step 5: specify external interfaces (1/2)
3
System A
System B
Flows exchanged
Key generic features of an interface

## Slide 14: Environment architecture – Step 5: specify external interfaces (2/2) Example of the external interface between a car and a gas station
3
Interface characteristics | Interface between fuel nozzle and car
Interacting systems | Car, fuel, fuel nozzle
Medium | fuel nozzle
Interaction type | Mechanical & chemical interactions
Exchanged flows | Fuel, gas & forces
Interface lifecycle | Interface access granted/not granted, fuel nozzle present/not present, fuel present/not present, …
Nominal operation | Plug the fuel nozzle onto the car and refuel
Abnormal operation | Fuel reflux, fuel tank blocked of choked
Interaction points | Fuel tank filling neck (inner), fuel nozzle (outer)
Constraints | The interface shall allow air flow to pass in order to equilibrate inner and outer pressure The interface shall withstand the lever induced by the fuel system
Each external interface of the target system shall be precisely described

## Slide 15: Course agenda
Introduction
Systems architecture key concepts & framework
Operational architecture and needs engineering
  3.1 – Environment architecture
  3.2 – Lifecycle definition
  3.3 – Needs architecture & allocation
  3.4 – Use case analysis
Requirements engineering
Functional architecture
1
2
3
4
5

## Slide 16: Lifecycle definition concepts Lifecycle & lifecycle phase
3
Integrated cooling module
The system lifecycle is the synthesis of its lifecycle phases, namely its life periods as perceived by its environment (customers, end-users, supporting systems, technical infrastructures, etc.) when the exchanges or use made with the system are stable
Events that trigger « immediately » an lifecycle phase change
Lifecycle phases modeled by states (of a state diagram)
Concurrent phases (i.e. in which the system can be at a same moment)

## Slide 17: Lifecycle definition process overview (2/2)
3
Identify
lifecycle phases
Step 1
Organise
lifecycle phases
Step 2
Organized lifecycle phases
Identify events
Step 3
Lifecycle phases
Preliminary lifecycle diagram
The lifecycle definition process intends to identify exhaustively the lifecycle phases of a given system
Cross check with environment and needs
Step 4
Mature lifecycle diagram

## Slide 18: Lifecycle definition process overview (1/2)
3
Generic situation 2
The lifecycle definition process allows to define the system lifecycle and its operational scenarios, which are the « entry points » for the functional analysis by:
  defining the system lifecycle
  defining a use case for each lifecycle phase involved in the system lifecycle
  analyzing the dynamic behavior of each use case by mean of an operational scenario
Use cases and operational scenarios will be studied on day 4.
Time
Event
Event
…
Event
Event
States / events
1
Generic situation 1
Generic situation 1
Generic situation2.1
Generic situation 2.2
Generic situation 2.3
Zoom on a lifecycle state modeling an lifecycle phase
2
Use case
Operational
scenario
3

## Slide 19: Course agenda
Introduction
Systems architecture key concepts & framework
Operational architecture and needs engineering
  3.1 – Environment architecture
  3.2 – Lifecycle definition
  3.3 – Needs architecture & allocation
  3.4 – Use case analysis
Requirements engineering
Functional architecture
1
2
3
4
5

## Slide 20: Overview of needs & requirements on a given system
3
Missions
Functions
Components
Functional level
Constructional
level
Operational level
Outside of the vehicle
Outside
Inside
In order to fulfill to the needs coming from the external systems of its environment (1), the vehicle shall behave in a certain way (2) and be structured in a certain manner (3-4).
Constructional requirements
Allocation relationships
Logiciels
Matériels
Software & hardware components
Missions
Functional requirements
2
Extended Vehicle
Function 1
Function 3
Derivation
relationships
Allocation relationships
Function 2
People
Organizational requirements
3
Function 4
Technical requirements
4
Needs
1
Environment
Be careful to the relativity of the point of views: a requirement on an external system is a need relatively to the system of interest
Derivation
relationships

## Slide 21: Need template
3
Need – Domain
Need template that shall be respected
A domain corresponds to a « relevant » set of external systems and/or stakeholders
Never forget this item, since it allows to reformulate the need in a more pertinent way
Need = expected characteristic or constraint imposed
by an external system

## Slide 22: Typical categories of needs
3
Types of requirements on an industrial system |  | 
O | Operability | Capability of being easily used by end-users, operators & technicians
A | Availability | Capability to remain in normal operational conditions (synthesizes maintainability & reliability)
P | Performance | Capability of ensuring specific services levels and/or economical objectives
S | Safety (resp. security) | Capability of functioning without (resp. with) negative impacts on (resp. from) the outside of the system
E | Evolutivity & durability | Capability of evolving among time and adapting to new stakeholders requirements
T | Transparency | Capability of reporting the internal views of the system of interest to the outside
Some typical categories of needs
Types of stakeholders requirements on an industrial system |  | Corresponding external systems
P | Political | Political system
E | Economical | Economical system
S | Social | Society
T | Technological | Technological innovation system
E | Environmental | Earth
L | Legal | Legal & regulatory system

## Slide 23: Needs architecture – Step 1: identify the needs capture methods
3
Production and maintenance
End users
Energy sources
Project System
Economy
Standards and Regulations
Vehicle system
Data
Constraints
Data
Data
Services
Energy
The first activity consists in identifying the methods for capturing needs (interviews with stakeholders, market research or study of a documentary corpus, brainstorming meetings)
Market research
Brainstor-ming
Corpus analyses
Interviews
Corpus analyses
Corpus analyses
Market research
Interviews
Stakeholders

## Slide 24: Needs architecture – Step 2: capture and formalize the needs
3
The second activity consists in formalizing the needs identified via the capture methods identified in the previous activity using a standardized template of needs.
Stakeholders
Needs
Formalized need: <Marketing> shall be able to <guarantee that the “Overall vehicle and front accessibility” service> (Marketing grid § 7) has <an overall efficiency mark of X> in <standard use> .
Need template: The <stakeholder> shall be able to <do something> with an <expected level of performance> in a <given lifecycle phase> .
Stakeholders interviews
Marketing briefing
Brainstorming
Needs capture methods
Document analysis
Analysis grid | Stakeholder | To do something | Level of performance | Lifecycle phase
 | Marketing | guarantee that the “Overall vehicle and front accessibility” service | an overall efficiency mark of X | standard use

## Slide 25: Good practices Needs coverage and consistency checks
3
Operability
Environment analysis show that operability category shall cover:
End-users operability
Technical operability
Maintenance operability
Support operability
…
(Partial) needs architecture
Support
operability
Standard tools imposes…
Maintenance team shall be able to…
Logistics imposes…
The assembly line shall be able to…
End-users operability
Technical
operability
The driver shall be able to….
Groupe PSA IT infrastructure imposes…
Maintenance
operability
The front passenger shall be able to…
Coverage relationships & needs architecture organization principles shall be checked in order to resolve all logical inconsistencies which can lead to reformulate the needs, to identify missing needs and/or to identify new topics
Vehicle

## Slide 26: Good practices Cross check analysis between needs and life cycle
3
Outside of the vehicle
Needs
Crossed operational analyses (needs  operational models) must also enable detection of missing elements and alignment of each specification
Lifecycle definition
The maintenance system shall be able to detect a braking failure when the vehicle is being revised.
1
Identification of the "maintenance" context
The maintenance system shall be able to tract the vehicle securely when the vehicle is towed to the garage.
2
Needs engineering
Identification of a need linked to the "towing" context
Vehicle

## Slide 27: Main difficulties of needs capture and classification (2/2)
3
Classical difficulty 1: technical intrusion
  Context: a stakeholder expresses a need as a requirement: « the system shall … ».
  Difficulty: it is impossible to express this need exploiting the proper template
  Good practice: try to understand what are the core reasons that are motivating the stakeholder and explore the associated causality chain (you shall find « the cause of the cause » up to 5 iterations …) in order to identify the real source need
Classical difficulty 2: apparent indifference
  Context: a stakeholder expresses a need that has apparently no relationships with the system of interest: « Airline pilots shall eat blueberries each day » …
  What shall not be done: do not ignore « a priori » that need since it may reveal important information on an “hidden” external influence
  Good practice: identify the nature of the interaction and/or interdependency that exists between the stakeholders and the system of interest and verify if a given apparently non relevant need has really an influence on the system of interest.

## Slide 28: Good practices Share & challenge formalized needs with their stakeholders
3
Vote on a set of stakeholders needs in a collaborative workshop
OK
NOT OK
To be reformulated
Sharing a set of needs: consensual rewording of contentious items and removal of unshared needs
Needs shall be always shared & challenged with all stakeholders in order to be sure that a system design starts on a solid & robust basis
Remember: the success of a collaborative workshop relies on the capability of gathering together all the stakeholders of the set of needs that have to be shared

## Slide 29: As a conclusion … varied perceptions on a given system
3
Always be in touch with the real needs, all along the development and integration cycle

## Slide 30: Course agenda
Introduction
Systems architecture key concepts & framework
Operational architecture and needs engineering
  3.1 – Environment architecture
  3.2 – Lifecycle definition
  3.3 – Needs architecture & allocation
  3.4 – Use case analysis
Requirements engineering
Functional architecture
1
2
3
4
5

## Slide 31: Use case analysis concepts Use case
3
A use case is a static specification of a lifecycle phase that describes both all external systems interacting with the system in the considered context and the associated interactions
Activities involving the target system
External systems
Lifecycle phase = Vehicle Key On
Target system boundary
Integrated cooling module

## Slide 32: … as the starting point of a “local” detailed operational architecture
3
All details cannot be mentioned on global views. Expertise of the architects teams can sort out the problems by providing a detailed operational architecture study relatively to their perimeter.

## Slide 33: Use case analysis concepts Operational scenario
3
An operational scenario is a dynamic specification that describes the dynamics of a given lifecycle phase of a system, namely the activities and the external exchanges that cover entirely the considered context.
External systems
Target system
Operational flow
Timeline
Integrated cooling module
Time
Target system boundary

## Slide 34: Use case analysis process
3
The main phases of the system use case analysis process
Identify and model use cases
Step 2
Use cases
System lifecycle
Choose
a lifecycle
phase
Lifecycle phase
Model operational scenarios
Step 3
Are there
remaining phases not analysed?
YES
NO
Operational
scenarios
Step 1

## Slide 35: Use case analysis – Steps 1&2: chose a lifecycle phase and identify & model use cases (1/2)
3
A use case related to a lifecycle phase can be described by:
- identifying all external systems that are involved in that lifecycle phase,
- making explicit the uses of the target system by those external systems which are interacting with it during the selected lifecycle phase.
Integrated cooling module
Vehicle key ON
Hint: try to formulate the following sentence
“The [external systems] are using the [system of interest] to [do something]”
The considered context

## Slide 36: Use case analysis – Steps 1&2: chose a lifecycle phase and identify & model use cases (2/2)
3
Having a use case table is mandatory to reflect the coverage of your study, but in some cases, presenting use cases using a diagram is to be preferred.
A use case diagram is more convenient to share and improve the study, but can be time costly
A use case table gives the global picture but is not collaborative friendly

## Slide 37: Use case analysis – Step 3: model operational scenarios (1/2) How to analyze an operational scenario?
3
An operational scenario of a system describes a chain of activities performed by the target system and a set of external systems which typically capture the dynamic behavior of a given use case (and thus the underlying lifecycle phase).
1
Identify the systems that are involved in the operational scenario considered
External systems involved in a use case
Identify the initiating event
Analyze the chain of activities existing between the systems
2
3
Target
system

## Slide 38: Use case analysis – Step 3: model operational scenarios (2/2) How to formalize an operational scenario?
3
The operational scenario associated to a dedicated use case can be built by:
finding all the involved (external & internal) systems,
identifying the first (initiating) event triggering the operational scenario,
analyzing the chain of activities performed by the involved systems and the nature of their exchanged flows during the underlying lifecycle phase.
Integrated cooling module
Use case
Provide nominal cockpit heating
Operational scenario
Corresponding dynamic description

## Slide 39: Some advanced modelling elements
3
System of interest
External system 1
External system 2
External system n
Operational flow
time
Operational flow
parallel
Operational flow
Operational flow
loop
[loop condition]
Operational flow
Operational flow
alt
[alt condition]
else sequence
ref
Reference to another use case
parallel: allows modelling sequences occurring in parallel
loop: allows modelling repeating sequence depending on a condition
alt: allows modelling sequences which execution depends on a condition
(if / then / else)
ref: calls another use case

## Slide 40: Relationship with stakeholders requirements engineering
3
If needs analyses were properly conducted, no new unidentified lifecycle phase shall be detected further. To confirm this point, it is however useful to go through each use case and to check systematically whether each need is covered by one or several use cases.
Use cases
Needs
Covering
The Vehicle Services Architect shall guarantee the maximum Failure probability in use after 15 years / 240000 km of the hazard ERC4-18 (Inopportune steering of the wheels ) is < 10-X.
The marketing imposes a vehicle overall unit cost below XXX € for all its technical configurations.
The driver shall be able to lock/unlock the overall passenger compartment, front & rear with a mark greater than XXX in the "Park" lifecycle phase.
The regulations impose that all vehicles respect the ECE regulation when applicable.

## Slide 41
Exercise support

## Slide 42: Needs architecture & allocation concept Need
3
The Vehicle Services Architect shall guarantee that the maximum failure probability of the hazard ERC4-18 (Inopportune steering of the wheels ) is < 10-X after 15 years / 240,000 km
The marketing imposes a vehicle overall unitary cost below XXX €
in any configuration.
The driver shall be able to lock/unlock the overall passenger compartment, front & rear with an efficiency greater than XXX in the "Park" lifecycle phase.
Regulations impose that all vehicles respect the ECE regulation when applicable.
Production and maintenance
Driver
Energy sources
Project System
Marketing
Standards and Regulations
Vehicle system
Stakeholder
A need relative to a system is an expected or imposed property by one or more external systems of its environment that has a impact on the system

## Slide 43: Needs architecture – Step 2: capture and formalize the needs Automotive illustration – Examples of needs
3
The regulation imposes all vehicles to respect the UNECE regulation in all phases
The marketing imposes a vehicle overall unitary cost below XXX € in manufacturing phase
  Some examples of needs expressed at vehicle system level that might impact the Integrated Cooling Module design
The plant imposes that the whole vehicle shall be assembled with respect to safety rules
XXXX and YYYY in mounting phase
The user shall be able to operate the vehicle in Europe, Russia and China in transition to use phase and operating phase
The marketing shall be able to demonstrate a cabin heating efficiency with a mark of 7 (see referential XXX) in operating phase
The owner shall be able to use the vehicle with a failure probability of 10-x after 15 years / 240 000 km in operating phase
Euro NCAP shall be able to deliver a mark of 4/5 at crash tests in design phase
Groupe PSA strategy imposes the powertrain to reach the performances mentioned in the roadmap XXX, in design phase

## Slide 44: Needs architecture – Step 2: capture and formalize the needs Automotive illustration – Examples of satisfaction criteria
3
Need | Satisfaction criteria
The plant imposes that the whole vehicle has to be assembled with respect to safety rules XXXX and YYYY in « mounting » phase | Design review Safety rules fulfillment assessment
The user shall be able to operate the vehicle in Europe, Russia and China in transition to use phase and operating phase | Climate bench tests
  Some examples of satisfaction criteria associated with given needs

## Slide 45: Needs architecture – Step 3: Classify needs into homogeneous sub-assemblies – Automotive illustration
3
  A possible (partial) classification of needs
Safety
The plant imposes that the whole vehicle has to be assembled with respect to safety rules XXXX and YYYY in « mounting » phase
Durability
Performance
The marketing imposes a vehicle overall unitary cost below XXX € in manufacturing phase
The marketing shall be able to demonstrate a cabin heating efficiency with a mark of 7 (see referential XXX) in operating phase
Operability
The user shall be able to operate the vehicle in Europe, Russia and China in transition
to use phase and operating phase
The owner shall be able to use the vehicle with a failure probability of 10-x after 15 years / 240 000 km in operating phase
Euro NCAP shall be able to deliver a mark of 4/5 at crash tests in design phase
Groupe PSA strategy imposes the powertrain to reach the performances mentioned in the roadmap XXX, in design phase