## Slide 1: Mini-Project Cellular Network Deployment

## Slide 2: Context Description
You have been delegated by a telecommunication operator to answer a tender call for radio planification, dimensioning and deployment of a cellular 4G network.
The network is deployed on a frequency carrier of 2.6 GHz and the base stations are connected among each others using microwave links (Faisceaux Hertziens).
There are different options considering different bandwidth size : 5, 10, 15 and 20 MHz. This corresponds respectively to 25, 50, 75 and 100 radio-resources.

## Slide 3: Mini-Project Objectives
Based on the following data, you need to define :
  The maximal tolerated path-loss in the uplink and in the downlink
  The radio coverage radius in the uplink and the downlink in cases in rural and urban zones
  Considering bandwidth sizes (5, 10, 15, 20) MHz, determine for rural and urban zones :
    The size of the cell that guarantees that the cell is well dimensioned
    The cell size that respects both radio and dimensioning constraints
    The optimised transmission power
    The cost of the network considering different bandwidth.
    The evolution of income/outcome and economical profitability.

## Slide 4: Environment Description
Carrier frequency = 2600 MHz
The zones to cover include :
We estimate that each client uses in average the network during 10 minutes each hour .
Zone | Area | Population | Penetration rate | Path-loss (dB) | Shadowing + Fading (dB)
Urban | 105,4 km2 | 1 750 000 | 10% | 113 + 35 log10 d | 8 + 2
Rural | 5176 km2 | 17 500 | 10% | 100 + 35 log10 d | 4 + 2
4

## Slide 5: Equipment Radio-Characteristics
Radio planning | Base station | Power of the Base station | 46 | dBm
 |  | Antenna gain | 17 | dB
 |  | Cables and connectors loss | 3 | dB
 |  | Duplexer | 2 | dB
 |  | Receiver diversity | 5 | dB
 |  | Low received power amplifier | 2 | dB
 |  | Sensisivity of reception | -120 | dBm
 | Mobile | Power of the mobile | 21 | dBm
 |  | antenna gain | 0 | dB
 |  | Internal loss | 0 | dB
 |  | Sensitivity of reception | -105 | dBm
5

## Slide 6: Resources
Ressources | Ratio of Signal / Interference C/I (no unit) | 1,14 |  |  | 
 | Frequency reuse pattern size | 1 |  |  | 
 | Bandwidth (MHz) | 5 | 10 | 15 | 20
 | Number of radio resources per cell | 25 | 50 | 75 | 100
 | Blockage probability | 2% | 2% | 2% | 2%
 | Traffic in Erlang per cell |  |  |  | 
 | Traffic per client |  |  |  | 
 | Number of clients per cell |  |  |  | 
6

## Slide 7: Costs
Income / Outcome | Costs
Fees for use of 2.6 GHz frequency in the uplink and downlink (5 MHz UL / 5 MHz DL) | 2500 k€
Fees for the use of 18 GHz frequency for microwave links to connect the base-stations | 100 k€
Capex : costs for installing the sites | 15 k€
Opex : operating Investments (electricity, maintenance, etc) | 5 k€
Price of client suscription | 20 €
7